Parts for Scope Clock

Capacitors                                                Potentiometers

2 - 4.7uF , 450V           (electrolytic)     1–50K or 47K-.25W top adjust (503 or 473)

5 - .1uF  (104)              (ceramic)          2-1M ,.25W top adjust (105)

1 - 1,000uF ,16 - 25V   (electrolytic)      2 - 50K , .12W side adjust

1 - 100uF , 10 - 25V     (electrolytic)      2 – 50K, .12W top adjust

1 - .01uF (103)             (ceramic)

Diodes                                             Miscellaneous

2 - 1N4007                                       3 - push buttons

3 - 1N4001                                       1 - DPDT Relay   9 – 12 V coil, non-latching

1 - Rectifier Bridge (25V #512-2KBP01M)

1 - 5V regulator        7805

IC Sockets                                       1 - 20MHZ XTAL

1 - 20 pin                                          1- four pin jumper

3 - 8  pin                                           1 - solder-in fuse

1 - 28 pin                                          1 - led

1 - neon lamp

Transformer  -120V/240V prim., 7-9 V sec

Wire

Transistors                                                                 GPS (Optional)

5 - MPSA44	(NPN)	                                                   GPS module

1 - MPSA92	(PNP)                                                    GPS antenna

2 - 2N3904    (NPN)                                                    5 pin edge socket

5 pin connector

Resistors  (1/4 Watt, unless otherwise noted)	     Chips

2 – 180K

5 - 47K   ( yellow purple orange ) 	                          PIC18f26k20

8 - 10K	   ( brown black orange ) 	               TLC7528 DAC

4 - 4.7	K  ( yellow purple red )	                           12f629 PIC

4 - 2.2		K  ( red  red  red  )	                           (2) 4032 digital rheostats -

2 - 330K  ( orange orange yellow )                            # 579-MCP 4132-103E/P

2 - 220K  (red red yellow )

1 - 1K     ( brown black red )                                     Battery backup

1 - 10M   ( brown black blue )                                   1 – nine volt battery clip

1 - 100K  ( brown black yellow )                               1 - relay

1 - 470 ohm  ( yellow purple brown )                        1 – 1N4001 diode

1 - 470K , ½ W   ( yellow purple yellow )                  1 – 470 ohm resistor

1 – 4.7 ohm , 1W  ( yellow purple gold)                       1 – 78L05 regulator

1 - 10 ohm , 3W  ( brown black black )                     1 – miniature led