Parts for Nixie 6.5

Capacitors                                                       Addt'l Caps for wall clock version

1 - 1,000uF , 35V                    (electrolytic)               1 – 1uF, 350VD

1 - 100uF - 220 uF, 25V          (electrolytic)               1 – 470uF, 25V

1 - 100uF - 220 uF, 6.3 -10V   (electrolytic)

3 - .01uF (103)                        (ceramic)                    1 – 47p (47)

1 - 10 uF, 6.3 - 10V                (electrolytic)                 1 – 2.2n (222)

2 - 2.2 uF, 350V (electrolytic) (Table clock version only)

Diodes                                             Miscellaneous

1 – Piezo Buzzer

2 - 1N4007 (table clock)                   4 - push buttons -3SPST & 1DPDT

4 - 1N4001                                       1 - DPDT Relay   12 V coil, non-latching

1 – BYV95C (wall clock)                  1 - Rectifier Bridge   25V #512-2KBP01M

1 - 5V regulator        7805

1 - 12V regulator      7812

IC Sockets                                         2 – Heat sinks

1 - 16 pin                                          1 - solder-in fuse

1 - 28 pin                                          1 - Red led 5mm

1 - 8 pin IC socket (wall clock only)  1 - Green led 5mm

6 – RGB leds or 6 blue leds 3mm

5 - neon lamp (4 colons, 1 indicator)

2- four pin jumper

Transformer  -120V/240V prim., 7-9 V sec

Wire & connectors

Transistors                                       1 – AC adapter & connector (wall clock only)

8 - MPSA44	(NPN)			    1 - 100uH, 1A coil (wall clock only)

7 - MPSA92	(PNP)                           1 - IRF730 power transistor (wall clock)

2 - 2N3904    (NPN)                           1 - 1K (102) trim pot (wall clock)

Resistors  (1/4 Watt, unless otherwise noted)	     Chips

6 - 47K   ( yellow purple orange ) 	                          PIC18f26k20

3 - 10K   ( brown black orange ) 		               74141 or equivalent

4 - 2.2K  ( red  red  red  )

2 - 220K  (red red yellow )                                         Battery backup

3 - 1K     ( brown black red )                                     1 – 1,000 uF, 6.3V

1 - 1M      (brown black green)                                 1 - nine volt battery clip

8 - 100K  ( brown black yellow )                               1 - 5VDC relay

3 - 470 ohm  ( yellow purple brown )                        2 - 1N4001 diode

1 - 220 ohm , ½ W  (red red brown)                         1 -10K resistor

8 - 33K      (orange orange orange)                          1 - 78L05 regulator

7 - 470K     (yellow purple yellow)                             1 – led

3 – 100 ohm

1 – 6.8K