EL-1663B-A wireless module

Description:

This module is a small size, low consumption and wireless transceiver module which adopts Silicon  Labs Si4463 B1 chip. It intergrated all peripheral components that modules needs. Users can contril chip internal register via digital I/O, to transmit, receive data and configurate the parameters.

Features:

Complete FSK, GFSK, OOK transceiver

Working frequency range: 433 ~ 470 MHZ (can be customized)

Transmitted power: A typical 19.8 dBm

Receiving sensitivity: - 123 - dBm@1.2Kbps

Open area communication distance is 2300 meters above the @ 1.2 Kbps

Data rate: maximum 500 KBPS

FSK frequency programmable (1 ~ 160 KHZ)

Programmable receiving bandwidth (10.6 ~ 230.4 KHz)

Just use six I/O port (SDI, SDO, SCK, NSEL, NIRQ, SDN) can get a job

SPI compatible control interface

Low-power task cycle model, bringing wake timer, low cut-off current (na)

Power supply: 1.8 V to 3.6 V

Low receive current (typically 18.5 mA)

Transmitting current (typically 80 ma)

Built-in temperature sensor and 8-bit ADC

Integrated voltage regulator

For narrowband systems, crystals with high precision, built-in crystal load capacitance tuning circuit, convenient production and debugging.

# Application:

wireless meter reading(

wireless sensor(

remote wireless data transmission(

home automation and security access control system(

vehicle anti-theft(

remote industrial remote control, remote sensing(

garage control(

wireless pager(

lighting control(

smart metering(

remote control(

family security and alarm(

garage door openers(

remote keyless entry(

automation(

industrial control(

sensor network(

# Pin:

| pin | name | type | description |
| --- | --- | --- | --- |
| 1 | GND | S | Power ground |
| 2 | VCC | S | Voltage supply |
| 3 | SDN | DI | Chip off mode input (valid in high level) 芯片关断模式输入（高电平有效） |
| 4 | nIRQ | DO | Interrupt request output (valid in low level) |
| 5 | nSEL | DI | SPI select input(valid in low level) |
| 6 | SCK | DI | SPI serial clock input |
| 7 | SDI | DO | SPI serial data input |
| 8 | SDO | DO | SPI serial data output |
| 9 | ANT | S | antenna |
| 10 | GND | S | ground |

# Configuration:

GPIO2 is transmitting control

GPIO3 is receiving control

// Configure the GPIOs

abApi_Write[0] = CMD_GPIO_PIN_CFG;  // Use GPIO pin configurationcommand

abApi_Write[1] = 0x10;               // Configure GPIO0 as Tx data CLK

abApi_Write[2] = 0x13;               // Configure GPIO1 as Tx data

abApi_Write[3] = 0x20;               // Configure GPIO2 as tx state

abApi_Write[4] = 0x21;               // Configure GPIO3 as rx state

bApi_SendCommand(5,abApi_Write);   // Send command to the radio IC

vApi_WaitforCTS();