EL4432B-A wireless module V1.1

Description:

This module is a small size, low consumption and wireless transceiver module which adopts Silicon  Labs Si4432 B1 chip. It intergrated all peripheral components that modules needs. Users can contril chip internal register via digital I/O, to transmit, receive data and configurate the parameters.

Features:

Complete FSK, GFSK, OOK transceiver

Working frequency range: 433 ~ 470 MHZ (can be customized)

Transmitted power: A typical 19.8 dBm

Receiving sensitivity: - 115 - dBm@9.6Kbps

Open area communication distance is 1200 meters above the @ 9.6 Kbps

Data rate: maximum 128 KBPS

FSK frequency programmable (1 ~ 160 KHZ)

Programmable receiving bandwidth (10.6 ~ 230.4 KHz)

Just use six I/O port (SDI, SDO, SCK, NSEL, NIRQ, SDN) can get a job

SPI compatible control interface

Low-power task cycle model, bringing wake timer, low cut-off current (na)

Power supply: 1.8 V to 3.6 V

Low receive current (typically 18.5 mA)

Transmitting current (typically 80 ma)

Built-in temperature sensor and 8-bit ADC

Integrated voltage regulator

For narrowband systems, crystals with high precision, built-in crystal load capacitance tuning circuit, convenient production and debugging.

Application:

Home automation and security access control system

Wireless meter reading

Vehicle anti-theft

Wireless sensor

Remote wireless data transmission

Remote industrial remote control, remote sensing

Pin:

| pin | name | type | description |
| --- | --- | --- | --- |
| 1 | GND | S | Power ground |
| 2 | VCC | S | Voltage supply |
| 3 | SDN | DI | Chip off mode input (valid in high level) 芯片关断模式输入（高电平有效） |
| 4 | nIRQ | DO | Interrupt request output (valid in low level) |
| 5 | nSEL | DI | SPI select input(valid in low level) |
| 6 | SCK | DI | SPI serial clock input |
| 7 | SDI | DO | SPI serial data input |
| 8 | SDO | DO | SPI serial data output |
| 9 | ANT | S | antenna |
| 10 | GND | S | ground |