CC2530 Zigbee module Datasheet

Feature:

__with PA+LNA chip, lead pin pitch 2.54mm,  SMA antenna

＿open frequency，carrier frequency 2.4GHz

＿air data rate 250kbps

＿16 channels

＿TTL 3.3V level/UART interface。Baud rate is 38400bps/8/N/1 by factory setting.

＿small size, embedded.

＿adopts SoC and high precise brand SMD crystal, stable!

Parameters:

| parameters | SZ3 | unit | Description |
| --- | --- | --- | --- |
| Working voltage | 3.3 | V |  |
| Transmitting current | 170 | mA | Output power +20dBm |
| Receiving current | 32 | mA |  |
| Standby current | 0.7 | uA |  |
| Working frequency | 2.405~2.485 | GHz |  |
| Output power | >21 | dBm |  |
| sensitivity | -108 | dBm |  |
| Air rate | 250 | Kbps |  |
| distance | 1200 | m | According to Antenna gain and height |
| Baud rate | 38400 | bps |  |
| Working temperature | -30～+70 | ℃ |  |
| size | 32×32 | mm |  |

Pin Definition:

| pin | name | Input/output | Description |
| --- | --- | --- | --- |
| 1 /B1 | RESET_N | input | Reset pin，input，low level reset |
| 2 /B2 | P0.0 | Input/output | CC2530 P0.0 |
| 3 /B3 | P0.1 | Input/output | CC2530 P0.1 |
| 4 /B4 | P0.2 (RX) | input | CC2530 P0.2 , UART RX |
| 5 /B5 | P0.3 (TX) | output | CC2530 P0.3 , UART TX |
| 6 /B6 | P0.4 | Input/output | CC2530 P0.4 |
| 7 /B7 | P0.5 | Input/output | CC2530 P0.5 |
| 8 /B8 | P0.6 | Input/output | CC2530 P0.6 |
| 9 /B9 | P0.7 | Input/output | CC2530 P0.7 |
| 10/B10 | P1.0 | Input/output | CC2530 P1.0 |
| 11/B11 | P1.1 | Input/output | CC2530 P1.1 PA is used |
| 12/B12 | P1.2 | Input/output | CC2530 P1.2 PA is used |
| 13/A12 | P1.3 | Input/output | CC2530 P1.3 |
| 14/A11 | P1.4 | Input/output | CC2530 P1.4 |
| 15/A10 | P1.5 | Input/output | CC2530 P1.5 |
| 16/A9 | P1.6 | Input/output | CC2530 P1.6 |
| 17/A8 | P1.7 | Input/output | CC2530 P1.7 |
| 18/A7 | P2.0 | Input/output | CC2530 P2.0 |
| 19/A6 | P2.1 | Input/output | CC2530 P2.1 |
| 20/A5 | P2.2 | Input/output | CC2530 P2.2 |
| 21/A4 | VCC | input | Power 3.3V |
| 22/A3 | VCC | input | Power 3.3V |
| 23/A2 | GND |  | Power ground |
| 24/A1 | GND |  | Power ground |

- All IO, including serial Uart, are 3.3V level.

- Ax ,Bx is the corresponding pin for SZ3 module.

3       Pin all leaded,   but P1_1,  P1_2 ps is for PA

| P1-1（TRX） | P1_2(CE) |  |
| --- | --- | --- |
| 1 | * | TxActive |
| 0 | 1 | RxActive |
| 0 | 0 | Chip is shut down |

Setting output power:

Advise users to set the output power into -4~-6dBm(TXPOWER is 0x85 or 0x95). At this time, the current is about 170mA. This will be the best.

(If the output setting is higher than -4dBm, the output power will come to +23.5dBm, but its current will come to over 200mA)