SRX882 Low Consumption Strong Driving Force Super Heterodyne Receiver Module

# Description

SRX882 is a micro power strong driving force super heterodyne receiver module. It is can support our transmitter module STX882/STX888. It has high stability, anti-interference and high cost-effective, also has a powerful driving force, certified by ROHS, FCC, CE, The module can be connected to the microcontroller directly. So it is more convenient for user developing wireless products

- Features

  - Frequency Range: 433/315 MHZ

  - ASK /OOK modulation mode

  - Super anti-power interference

  - Low-power sleep less than 1uA

  - Low self radiation

  - Small size

  - Frequency stability and reliability

Various international testing standards

- Application

  - Remote door

  - Wireless security alarm

  - Wireless industrial control

  - Wireless data transmission

- Electronic Specification

| Parameter | Min | TP | Max | Unit | Condition |
| --- | --- | --- | --- | --- | --- |
| Operation conditions |
| Supply Voltage | 2.4 | 5 | 5.5 | V |  |
| Operating Temperature Range | -30 |  | 85 | ℃ |  |
| Latency |  |  | 20 | ms | @315MHZ |
|  |  |  | 9 | ms | @433@HZ |
| Current consumption |
| Consuming current |  | 2.5 |  | mA | @315MHZ |
|  |  | 2.8 |  | mA | @433MHZ |
|  |  | ＜2 |  | uA | @CS=1 Or vacant |
| RF parameters |
| Frequency Range | 433.82 | 433.92 | 434.02 | MHZ | @433MHZ |
|  | 314.9 | 315 | 315.1 | MHZ | @315MHZ |
| Sensitivity |  | -110 | -107 | dBm | @1.2Kbps |
| Air rate | 0.1 |  | 9.6 | kbps |  |
| Receiver bandwidth |  | 200 |  | KHz |  |

- Pin definition

| Pin Number | Pin Definitions | Description |
| --- | --- | --- |
| 1 | ANT | Matching 50 ohm antenna |
| 2 | GND | Connected to power ground |
| 3 | VCC | Positive power supply |
| 4 | CS | High level to enable the module, low level to enter sleep mode |
| 5 | DATA | Data output pin |
| 6 | GND | Connected to power ground |
| 7 | ANT | Matching 50 ohm antenna |

- Mechanical Size